Enterprise Control Configuration and Logging framework
SNMP Alarms Operation

Copyright (C) 2013 Free Software Foundation.

Permission is granted to copy, distribute and/or modify this document under the terms of the GNU Free Documentation License, Version 1.3 or any later version published by the Free Software Foundation; with no Invariant Sections, no Front-Cover Texts, and no Back-Cover Texts.
A copy of the license is included in the section entitled "GNU Free Documentation License".

PURPOSE
The purpose of this document is to describe the integration of the Enterprise Control Configuration and Logging (ECCL) framework's alarm mechanism into an SNMP monitored network.

Alarms to a management system will be delivered via an SNMP V2 agent. The alarms will report problems affecting the operation of the software system (and possibly associated hardware) which is making use of ECCL. These may include database alarms, network alarms, processing alarms, hardware: disk full, memory full, etc.

The characteristics of the MIB are described in this document, though the MIB itself (with its own internal documentation) is supplied separately.

REFERENCES
 CCITT X.721; Probabale cause values implemented by ECCL, available at http://www.itu.int/rec/T-REC-X.721/en
CCITT X.733; The alarm specification implemented by ECCL, available at http://www.itu.int/rec/T-REC-X.733/en
RFC1157; The 'coldstart' trep is specified at http://www.ietf.org/rfc/rfc1157.txt

DEFINITIONS
Agent: a software entity which provides SNMP information for a machine.
MIB (Management Information Base); a set of information organised in hierarchies and accessed via SNMP.
Control process; The process using the ECCL framework to implement alarm functionality (as part of an Agent) for a system.
NNM (Network Node Manager): a network element that handles SNMP traps and may issue queries to an Agent.
SNMP (Simple Network Management Protocol): used for the remote management of network devices, such as switches, routers and servers.
Trap: the SNMP mechanism through which the Agent notifies the NNM of an alarm status.

DEVELOPMENT

Introduction
While SNMP has many faults as a system integration protocol, it is the only commonly used standard within large scale networks, and it is therefore the most reasonable choice for any software intended to integrate into such networks.
In attempts to make SNMP practically useful, a series of recommendations for SNMP agents have been developed. The ECCL framework implements one of these: the CCITT X.733 specification for alarms.
There are two vital elements in the SNMP architecture: the agent (software that each supplier must provide for an individual subsystem) and the manager (monitoring/management application). It can be viewed as a client-server architecture where the agent is the server and the manager is the client.
While the manager may query individual agents (acting as a client), it can also receive unsolicited events (traps) sent by the various agents, so in this respect the manager acts more like a server and the agent more like a client.
A manager can only carry out two operations on an agent: request or modify the information of an MIB variable of the agent. These operations are known as get-request and set-request.
The agent must implement the said operations with the following commands: GET (gathers the value of an object of the MIB), GETNEXT (gathers the value of the next object of the MIB to the OID requested), GETBULK (can run through the MIB tree to detect all of its objects) and SET (can modify the values of MIB’s variables).
The information provided by the agents to the manager is stored in the MIB (Management Information Base). The MIB has a tree-shaped hierarchic structure where there is only one path to reach a variable. The definition of a particular MIB element also specifies the type of data it can contain. The elements of a MIB can store whole numbers, strings and more complex structures, such as tables. The objects managed are the tree’s leaf nodes of the MIB.
A Managed Object (MO) is a resource that can be managed. An abstraction of the resource that represents its properties under the management point of view. A Managed Object is defined by its attributes, the operations that can be carried out, the notifications it can send and the relations with other objects managed.
We can have various kinds of Managed Objects:
- A machine's processes
- A logical connection between two entities
- A software subsystem within a process
- A hardware device

ECCL alarms are pushed to the manager as traps, but are also available for the manager to read from the database in the SNMP agent running on the machine hosting the ECCL software.

IMPLEMENTATION

The agent will send alarms for any event that has an impact on the platform.
- The ECCL agent code is implemented in a software module usually incorporated into the 'Control process', as an extension to the net-snmp agent (standard on most GNU/Linux and recent Solaris systems) using the 'Agent-X' extension protocol.
- The agent (net-snmp) must be configured to make the Agent-X protocol available (so that the ECCL Control process can act as an agent extension), and must be configured to forward traps to the NNM.
- The agent supports the standard snmpget, snmpset and snmpwalk operations on the ECCL MIB by forwarding the requests to the Control process, and the Control process sends traps by passing them to the agent (for forwarding on to the NNM).
- References to the 'Agent' and the 'Control process' are therefore commonly interchangeable as some functionality will reside in the net-snmp agent itself, while other functionality will reside in the Control process acting as an extension of the agent.
- The agent will allow the user (NNM) to browse each and every branch of the MIB; all variables will provide complete information. The NNM is therefore able to examine the alarm state of the system, in addition to receiving traps notifying it of changes.
- All alarms have a single numerical identifier (notificationID) for each agent. Clears will be sent through notificationID, objectID and the severity, i.e., the trap with:
- notificationID=1,
- objectID=objectTableIndex
- perceivedSeverity=Critical
  will be terminated with the trap with:
- notificationID=1
- objectID=objectTableIndex
- perceivedSeverity=Clear
- All alarms will have a clear. The framework never sends a clear trap if an alarm activation trap has not been sent before. Each alarm-clear grouping is defined as a correlation.
- Both the alarm and clear will have the same values in the following fields to achieve a correlation between them: objectID, probableCauseID, eventTypeID and specificProblem or more simply, in the objectID and notificationID fields.
- When the Control process detects a fault, it will only send one alarm. The alarm will not be sent again (though it may be cleared and then a new alarm may be sent).
- If an alarm changes its severity, its clear will be sent first and the alarm with the new severity next.
- The Control process maintains the table with the active alarms in order to facilitate the resynchronization between the manager and agent in the following cases: agent error, manager error, loss of connectivity and loss of traps (jumps in the trap sequence number). The active alarm table contains all information required to make sure that the NMM can generate the alarm in resynchronization processes. It contains the same fields indicated for the trap, except the trapSequenceNumber.
- After a crash (eg hardware failure) and subsequent start-up of the Control process, the Control process will update the active alarm table with the current situation of the system. It will do this before sending the coldstart (see RFC 1157). Therefore, when the NNM receives a coldstart trap and starts the resynchronization process, it will be able to gather all alarms related to the current state of the system.
- The resyncFlag variable defined in the MIB indicates whether a resynchronization process is being carried out (resyncFlag=1) or not (resyncFlag=0). Before sending a trap, the variable is checked to tell whether the resynchronization process is active or not. The traps will only be sent to the NNM if there is no active resynchronization process.
- When the resyncFlag variable is set (in other words, during the resynchronization process), the Control process will store the traps generated in the platform. When the variable is cleared (set to 0), the stored traps will be sent. Therefore, after the end of the resynchronization process, the manager and agent will be fully synchronized.
- If the resynchronization process is not active when an alarm clear occurs, the clear trap will be sent and the alarm corresponding to that clear will be deleted from the alarm table
- The Control process has a table for each alarm component, object, application or service. The objectsTable stores the names of all platform objects that can generate an alarm in a string. These strings are important – the names of the managed objects – and are formed of four fields:
- Field 1 = Host logical name (usually the fully qualified domain name of the host)
- Field 2 = Process logical name (an abstract process name)
- Filed 3 = Instance number (where multiple copies of a process are running)
- Field 4 = Component (software or hardware subsystem handled by the process)
- This string will comply with the following specifications:
- The fields will be separated by low dashes (underscores).
- No accents or special characters that can not be printed are allowed.
- The length of the string must not exceed 127 characters (it may be zero).
- The agent guarantees that the alarm object is in the alarm objectTable before a trap is sent that affects the object.
- The agent stores the sequence number of the last trap sent in the memory. If the agent stops working, the next trap number sent will be consecutive to the last number sent after start-up.
- The agent provides a mechanism to supervise this process. To do so, it will send a heart-beat trap every X (default is 5) minutes, which can be configured with the pollHeartBeat variable. This trap will only include the fields stated below. The information in this variable is not modified, even when the agent starts/stops.

The agent fills in the trap variables as follows:
- trapSequenceNumber: sequence number of the traps sent to the NNM. Whole number, 32 bits. This field is used to detect potential traps lost.
- notificationID: single identifier of each alarm, which will be used as the identifier to correlate the events associated to the same alarm. Whole number, 32 bits.
- perceivedSeverity: severity of the alarm. Whole number, 32 bits.
- FirstEventDate: this field is a string with the date and hour when the event was generated for the first time. Format: YYYYMMDD HH:MM:SS [optional]
- eventDate: this field is a string with the date and hour when the event was generated. Format: YYYYMMDD HH:MM:SS
- objectID: indicates the object affected by the alarm. This is the index of the managed object in the alarm object table.
- probableCauseID: number that identifies the probable cause of the event (integer, adjusted to the X.733 recommendation)
- eventTypeID: number that identifies the type of event notified. This indicates the alarm category. There are five types of events:
- Communications: this type of alarm is associated to the procedures and/or processes used to transfer information from one point to the other.
- Quality of service: the alarm is associated to the degradation of the quality of service.
- Processing error: the alarm is associated to software faults.
- Equipment: the alarm is associated to hardware faults.
- Environmental: this type of alarm is associated to the equipment environment.
- specificProblem: text string that will provide additional information about the probableCauseID field.
- proposedRepairAction: a text string used to suggest one or more solutions to the fault detected.
- additionalText: this field will contain any additional information that clarifies the cause and location of the error. For example, in the case of the HOST1_PROC2__ object, “90% CPU Use”]
- trendIndicator: Description of the alarm trend. The following values can be used:
- (zero) ==> First time the event takes place.
- + (positive sign) ==> The importance of the alarm is greater than that of the last alarm.
- - (negative sign) ==> The importance of the alarm is lower than that of the last alarm.

For the periodic heartbeat (as outlined above), the trap information is as follows:
- trapSequenceNumber: the corresponding number.
- notificationID: always the same number (999999).
- perceivedSeverity: warning
- firstEventDate: not required (null)
- eventDate: the corresponding date
- objectID: not required (null)
- probableCauseID: 0
- eventTypeID: 2
- specificProblem: not required (null)
- proposedRepairAction: not required (null)
- additionalText: “HEARTBEAT TRAP”
- trendIndicator: not required (null)

Alarm types
The X.733 specification is, understandably, mostly concerned with telecoms networks at the time it was written (over twenty years ago) and therefore provides many alarm types and probable causes for dealing with equipment and networking failures. In the modern world most systems alarms will actually be either of the Quality of service or Processing error types.

More common probable cause values are:
- ApplicationSubsystemFailure (2): some software subsystem failed
- ConfigurationOrCustomizationError (7): if missing or inconsistent configuration is detected
- LANError (25): if a network connection to another software component is lost or cannot be established
- QueueSizeExceeded (39): if some internal queue reaches a limit because items are added faster than they can be taken off (possibly the fault of a remote system not accepting requests quickly enough).
- RemoteNodeTransmissionError (42): if expected input from a remote system is not received
- LocalNodeTransmissionError (27): if expected output to a remote system cannot take place (I/O blocked)
- UnderlyingResourceUnavailable (56): if some necessary data is missing (eg a data file is missing or a database cannot be contacted)
- VersionMismatch (57): on software or protocol versioning missmatch

Probable cause codes
The generic field values used for alarms are listed in the MIB, however the integer value for the probableCause field is not in the MIB. The probableCause values are derived from the CCITT X.721 specification, with each value being an integer equal to the rightmost part of the OID defined in the X.721 specification. For example the OID 'adapterError' {9.3.2.0.0.1} is represented as the integer 1 and 'outOfMemory' {9.3.2.0.0.32} is represented as 32.
A full reference of the probable cause values may therefore be obtained from the X.721 document (or from the EcAlarm.h header file in the ECCL framework source code).

GNU Free Documentation License
Version 1.3, 3 November 2008
Copyright © 2000, 2001, 2002, 2007, 2008 Free Software Foundation, Inc. <http://fsf.org/>
Everyone is permitted to copy and distribute verbatim copies of this license document, but changing it is not allowed.
0. PREAMBLE
The purpose of this License is to make a manual, textbook, or other functional and useful document "free" in the sense of freedom: to assure everyone the effective freedom to copy and redistribute it, with or without modifying it, either commercially or noncommercially. Secondarily, this License preserves for the author and publisher a way to get credit for their work, while not being considered responsible for modifications made by others.
This License is a kind of "copyleft", which means that derivative works of the document must themselves be free in the same sense. It complements the GNU General Public License, which is a copyleft license designed for free software.
We have designed this License in order to use it for manuals for free software, because free software needs free documentation: a free program should come with manuals providing the same freedoms that the software does. But this License is not limited to software manuals; it can be used for any textual work, regardless of subject matter or whether it is published as a printed book. We recommend this License principally for works whose purpose is instruction or reference.
1. APPLICABILITY AND DEFINITIONS
This License applies to any manual or other work, in any medium, that contains a notice placed by the copyright holder saying it can be distributed under the terms of this License. Such a notice grants a world-wide, royalty-free license, unlimited in duration, to use that work under the conditions stated herein. The "Document", below, refers to any such manual or work. Any member of the public is a licensee, and is addressed as "you". You accept the license if you copy, modify or distribute the work in a way requiring permission under copyright law.
A "Modified Version" of the Document means any work containing the Document or a portion of it, either copied verbatim, or with modifications and/or translated into another language.
A "Secondary Section" is a named appendix or a front-matter section of the Document that deals exclusively with the relationship of the publishers or authors of the Document to the Document's overall subject (or to related matters) and contains nothing that could fall directly within that overall subject. (Thus, if the Document is in part a textbook of mathematics, a Secondary Section may not explain any mathematics.) The relationship could be a matter of historical connection with the subject or with related matters, or of legal, commercial, philosophical, ethical or political position regarding them.
The "Invariant Sections" are certain Secondary Sections whose titles are designated, as being those of Invariant Sections, in the notice that says that the Document is released under this License. If a section does not fit the above definition of Secondary then it is not allowed to be designated as Invariant. The Document may contain zero Invariant Sections. If the Document does not identify any Invariant Sections then there are none.
The "Cover Texts" are certain short passages of text that are listed, as Front-Cover Texts or Back-Cover Texts, in the notice that says that the Document is released under this License. A Front-Cover Text may be at most 5 words, and a Back-Cover Text may be at most 25 words.
A "Transparent" copy of the Document means a machine-readable copy, represented in a format whose specification is available to the general public, that is suitable for revising the document straightforwardly with generic text editors or (for images composed of pixels) generic paint programs or (for drawings) some widely available drawing editor, and that is suitable for input to text formatters or for automatic translation to a variety of formats suitable for input to text formatters. A copy made in an otherwise Transparent file format whose markup, or absence of markup, has been arranged to thwart or discourage subsequent modification by readers is not Transparent. An image format is not Transparent if used for any substantial amount of text. A copy that is not "Transparent" is called "Opaque".
Examples of suitable formats for Transparent copies include plain ASCII without markup, Texinfo input format, LaTeX input format, SGML or XML using a publicly available DTD, and standard-conforming simple HTML, PostScript or PDF designed for human modification. Examples of transparent image formats include PNG, XCF and JPG. Opaque formats include proprietary formats that can be read and edited only by proprietary word processors, SGML or XML for which the DTD and/or processing tools are not generally available, and the machine-generated HTML, PostScript or PDF produced by some word processors for output purposes only.
The "Title Page" means, for a printed book, the title page itself, plus such following pages as are needed to hold, legibly, the material this License requires to appear in the title page. For works in formats which do not have any title page as such, "Title Page" means the text near the most prominent appearance of the work's title, preceding the beginning of the body of the text.
The "publisher" means any person or entity that distributes copies of the Document to the public.
A section "Entitled XYZ" means a named subunit of the Document whose title either is precisely XYZ or contains XYZ in parentheses following text that translates XYZ in another language. (Here XYZ stands for a specific section name mentioned below, such as "Acknowledgements", "Dedications", "Endorsements", or "History".) To "Preserve the Title" of such a section when you modify the Document means that it remains a section "Entitled XYZ" according to this definition.
The Document may include Warranty Disclaimers next to the notice which states that this License applies to the Document. These Warranty Disclaimers are considered to be included by reference in this License, but only as regards disclaiming warranties: any other implication that these Warranty Disclaimers may have is void and has no effect on the meaning of this License.
2. VERBATIM COPYING
You may copy and distribute the Document in any medium, either commercially or noncommercially, provided that this License, the copyright notices, and the license notice saying this License applies to the Document are reproduced in all copies, and that you add no other conditions whatsoever to those of this License. You may not use technical measures to obstruct or control the reading or further copying of the copies you make or distribute. However, you may accept compensation in exchange for copies. If you distribute a large enough number of copies you must also follow the conditions in section 3.
You may also lend copies, under the same conditions stated above, and you may publicly display copies.
3. COPYING IN QUANTITY
If you publish printed copies (or copies in media that commonly have printed covers) of the Document, numbering more than 100, and the Document's license notice requires Cover Texts, you must enclose the copies in covers that carry, clearly and legibly, all these Cover Texts: Front-Cover Texts on the front cover, and Back-Cover Texts on the back cover. Both covers must also clearly and legibly identify you as the publisher of these copies. The front cover must present the full title with all words of the title equally prominent and visible. You may add other material on the covers in addition. Copying with changes limited to the covers, as long as they preserve the title of the Document and satisfy these conditions, can be treated as verbatim copying in other respects.
If the required texts for either cover are too voluminous to fit legibly, you should put the first ones listed (as many as fit reasonably) on the actual cover, and continue the rest onto adjacent pages.
If you publish or distribute Opaque copies of the Document numbering more than 100, you must either include a machine-readable Transparent copy along with each Opaque copy, or state in or with each Opaque copy a computer-network location from which the general network-using public has access to download using public-standard network protocols a complete Transparent copy of the Document, free of added material. If you use the latter option, you must take reasonably prudent steps, when you begin distribution of Opaque copies in quantity, to ensure that this Transparent copy will remain thus accessible at the stated location until at least one year after the last time you distribute an Opaque copy (directly or through your agents or retailers) of that edition to the public.
It is requested, but not required, that you contact the authors of the Document well before redistributing any large number of copies, to give them a chance to provide you with an updated version of the Document.
4. MODIFICATIONS
You may copy and distribute a Modified Version of the Document under the conditions of sections 2 and 3 above, provided that you release the Modified Version under precisely this License, with the Modified Version filling the role of the Document, thus licensing distribution and modification of the Modified Version to whoever possesses a copy of it. In addition, you must do these things in the Modified Version:
A. Use in the Title Page (and on the covers, if any) a title distinct from that of the Document, and from those of previous versions (which should, if there were any, be listed in the History section of the Document). You may use the same title as a previous version if the original publisher of that version gives permission.
B. List on the Title Page, as authors, one or more persons or entities responsible for authorship of the modifications in the Modified Version, together with at least five of the principal authors of the Document (all of its principal authors, if it has fewer than five), unless they release you from this requirement.
C. State on the Title page the name of the publisher of the Modified Version, as the publisher.
D. Preserve all the copyright notices of the Document.
E. Add an appropriate copyright notice for your modifications adjacent to the other copyright notices.
F. Include, immediately after the copyright notices, a license notice giving the public permission to use the Modified Version under the terms of this License, in the form shown in the Addendum below.
G. Preserve in that license notice the full lists of Invariant Sections and required Cover Texts given in the Document's license notice.
H. Include an unaltered copy of this License.
I. Preserve the section Entitled "History", Preserve its Title, and add to it an item stating at least the title, year, new authors, and publisher of the Modified Version as given on the Title Page. If there is no section Entitled "History" in the Document, create one stating the title, year, authors, and publisher of the Document as given on its Title Page, then add an item describing the Modified Version as stated in the previous sentence.
J. Preserve the network location, if any, given in the Document for public access to a Transparent copy of the Document, and likewise the network locations given in the Document for previous versions it was based on. These may be placed in the "History" section. You may omit a network location for a work that was published at least four years before the Document itself, or if the original publisher of the version it refers to gives permission.
K. For any section Entitled "Acknowledgements" or "Dedications", Preserve the Title of the section, and preserve in the section all the substance and tone of each of the contributor acknowledgements and/or dedications given therein.
L. Preserve all the Invariant Sections of the Document, unaltered in their text and in their titles. Section numbers or the equivalent are not considered part of the section titles.
M. Delete any section Entitled "Endorsements". Such a section may not be included in the Modified Version.
N. Do not retitle any existing section to be Entitled "Endorsements" or to conflict in title with any Invariant Section.
O. Preserve any Warranty Disclaimers.
If the Modified Version includes new front-matter sections or appendices that qualify as Secondary Sections and contain no material copied from the Document, you may at your option designate some or all of these sections as invariant. To do this, add their titles to the list of Invariant Sections in the Modified Version's license notice. These titles must be distinct from any other section titles.
You may add a section Entitled "Endorsements", provided it contains nothing but endorsements of your Modified Version by various parties—for example, statements of peer review or that the text has been approved by an organization as the authoritative definition of a standard.
You may add a passage of up to five words as a Front-Cover Text, and a passage of up to 25 words as a Back-Cover Text, to the end of the list of Cover Texts in the Modified Version. Only one passage of Front-Cover Text and one of Back-Cover Text may be added by (or through arrangements made by) any one entity. If the Document already includes a cover text for the same cover, previously added by you or by arrangement made by the same entity you are acting on behalf of, you may not add another; but you may replace the old one, on explicit permission from the previous publisher that added the old one.
The author(s) and publisher(s) of the Document do not by this License give permission to use their names for publicity for or to assert or imply endorsement of any Modified Version.
5. COMBINING DOCUMENTS
You may combine the Document with other documents released under this License, under the terms defined in section 4 above for modified versions, provided that you include in the combination all of the Invariant Sections of all of the original documents, unmodified, and list them all as Invariant Sections of your combined work in its license notice, and that you preserve all their Warranty Disclaimers.
The combined work need only contain one copy of this License, and multiple identical Invariant Sections may be replaced with a single copy. If there are multiple Invariant Sections with the same name but different contents, make the title of each such section unique by adding at the end of it, in parentheses, the name of the original author or publisher of that section if known, or else a unique number. Make the same adjustment to the section titles in the list of Invariant Sections in the license notice of the combined work.
In the combination, you must combine any sections Entitled "History" in the various original documents, forming one section Entitled "History"; likewise combine any sections Entitled "Acknowledgements", and any sections Entitled "Dedications". You must delete all sections Entitled "Endorsements".
6. COLLECTIONS OF DOCUMENTS
You may make a collection consisting of the Document and other documents released under this License, and replace the individual copies of this License in the various documents with a single copy that is included in the collection, provided that you follow the rules of this License for verbatim copying of each of the documents in all other respects.
You may extract a single document from such a collection, and distribute it individually under this License, provided you insert a copy of this License into the extracted document, and follow this License in all other respects regarding verbatim copying of that document.
7. AGGREGATION WITH INDEPENDENT WORKS
A compilation of the Document or its derivatives with other separate and independent documents or works, in or on a volume of a storage or distribution medium, is called an "aggregate" if the copyright resulting from the compilation is not used to limit the legal rights of the compilation's users beyond what the individual works permit. When the Document is included in an aggregate, this License does not apply to the other works in the aggregate which are not themselves derivative works of the Document.
If the Cover Text requirement of section 3 is applicable to these copies of the Document, then if the Document is less than one half of the entire aggregate, the Document's Cover Texts may be placed on covers that bracket the Document within the aggregate, or the electronic equivalent of covers if the Document is in electronic form. Otherwise they must appear on printed covers that bracket the whole aggregate.
8. TRANSLATION
Translation is considered a kind of modification, so you may distribute translations of the Document under the terms of section 4. Replacing Invariant Sections with translations requires special permission from their copyright holders, but you may include translations of some or all Invariant Sections in addition to the original versions of these Invariant Sections. You may include a translation of this License, and all the license notices in the Document, and any Warranty Disclaimers, provided that you also include the original English version of this License and the original versions of those notices and disclaimers. In case of a disagreement between the translation and the original version of this License or a notice or disclaimer, the original version will prevail.
If a section in the Document is Entitled "Acknowledgements", "Dedications", or "History", the requirement (section 4) to Preserve its Title (section 1) will typically require changing the actual title.
9. TERMINATION
You may not copy, modify, sublicense, or distribute the Document except as expressly provided under this License. Any attempt otherwise to copy, modify, sublicense, or distribute it is void, and will automatically terminate your rights under this License.
However, if you cease all violation of this License, then your license from a particular copyright holder is reinstated (a) provisionally, unless and until the copyright holder explicitly and finally terminates your license, and (b) permanently, if the copyright holder fails to notify you of the violation by some reasonable means prior to 60 days after the cessation.
Moreover, your license from a particular copyright holder is reinstated permanently if the copyright holder notifies you of the violation by some reasonable means, this is the first time you have received notice of violation of this License (for any work) from that copyright holder, and you cure the violation prior to 30 days after your receipt of the notice.
Termination of your rights under this section does not terminate the licenses of parties who have received copies or rights from you under this License. If your rights have been terminated and not permanently reinstated, receipt of a copy of some or all of the same material does not give you any rights to use it.
10. FUTURE REVISIONS OF THIS LICENSE
The Free Software Foundation may publish new, revised versions of the GNU Free Documentation License from time to time. Such new versions will be similar in spirit to the present version, but may differ in detail to address new problems or concerns. See http://www.gnu.org/copyleft/.
Each version of the License is given a distinguishing version number. If the Document specifies that a particular numbered version of this License "or any later version" applies to it, you have the option of following the terms and conditions either of that specified version or of any later version that has been published (not as a draft) by the Free Software Foundation. If the Document does not specify a version number of this License, you may choose any version ever published (not as a draft) by the Free Software Foundation. If the Document specifies that a proxy can decide which future versions of this License can be used, that proxy's public statement of acceptance of a version permanently authorizes you to choose that version for the Document.
11. RELICENSING
"Massive Multiauthor Collaboration Site" (or "MMC Site") means any World Wide Web server that publishes copyrightable works and also provides prominent facilities for anybody to edit those works. A public wiki that anybody can edit is an example of such a server. A "Massive Multiauthor Collaboration" (or "MMC") contained in the site means any set of copyrightable works thus published on the MMC site.
"CC-BY-SA" means the Creative Commons Attribution-Share Alike 3.0 license published by Creative Commons Corporation, a not-for-profit corporation with a principal place of business in San Francisco, California, as well as future copyleft versions of that license published by that same organization.
"Incorporate" means to publish or republish a Document, in whole or in part, as part of another Document.
An MMC is "eligible for relicensing" if it is licensed under this License, and if all works that were first published under this License somewhere other than this MMC, and subsequently incorporated in whole or in part into the MMC, (1) had no cover texts or invariant sections, and (2) were thus incorporated prior to November 1, 2008.
The operator of an MMC Site may republish an MMC contained in the site under CC-BY-SA on the same site at any time before August 1, 2009, provided the MMC is eligible for relicensing.